## Slide 1: Simulation and Modeling
CSE4131_CSE4132

## Slide 2: Reference Book
Computer Graphics (2nd Edition)
  D. HEARN
  M. P. BAKER

## Slide 3: Some Commonly Used Splines
Some commonly used Splines and their matrix and blending-function specifications
  Cubic Spline Interpolation Method
    Natural Cubic Splines
    Hermit Spline
    Cardinal Splines
    Kochanek-Bartels Splines

## Slide 4: Kochanek-Bartels Splines
These interpolating cubic polynomials are extensions of the cardinal Splines.
Two additional parameters are introduced into the constraint equations defining Kochanek-Bartels splines to provide for further flexibility in adjusting the shape of curve sections.

## Slide 5: Kochanek-Bartels Splines
Given four consecutive control points, labeled pk-1, pk, pk+1, and Pk+2, we define the boundary conditions for a Kochanek-Bartels curve section between pk and pk+ I as:
where t is the tension parameter, b is the bias parameter, and c is the continuity parameter.
In the Kochanek-Bartels formulation, parametric derivatives may not be continuous across section boundaries

## Slide 6: Kochanek-Bartels Splines
Tension parameter t has the same interpretation as in the cardinal-spline formulation;
  that is, it controls the looseness or tightness of the curve sections.
  Bias (b) is used to adjust the amount that the curve bends at each end of a section
    so that curve sections can be skewed toward one end or the other (Fig. 10-33).
  Parameter c controls the continuity of the tangent vector across the boundaries of sections.
    If c is assigned a nonzero value, there is a discontinuity in the slope of the curve across section boundaries.

## Slide 7: SPLINE
Spline
  Interpolation
    Cubic Spline Interpolation Method
      Natural Cubic Splines
      Hermit Spline
      Cardinal Splines
      Kochanek-Bartels Splines
  Approximation
    Bezier curves and surfaces
    B-spline curves and surfaces
    Beta-Splines
    Rational Splines

## Slide 8: BEZIER CURVES AND SURFACES
This spline approximation method was developed by the French engineer Pierre Bezier for use in the design of Renault automobile bodies.
Reasons of popularity:
  Bezier Splines have a number of properties that make them highly useful and convenient for curve and surface design.
  They are also easy to implement

## Slide 9: BEZIER CURVES AND SURFACES
Suppose we are given n + 1 control-point positions: pk = (xk, yk, zk), with k varying from 0 to n.
These coordinate points can be blended to produce the following position vector P(u), which describes the path of an approximating Bezier polynomial function between p0 and pn.
Eq. 10.40
The Bezier blending functions BEZk,n(U) are the Bernstein polynomials:
where the C(n, k) are the binomial coefficients:
Eq. 10.41
Eq. 10.42

## Slide 10: BEZIER CURVES AND SURFACES

## Slide 12: BEZIER CURVES AND SURFACES
Equivalently, we can define Bezier blending functions with the recursive calculation:
Eq. 10.40
Vector equation 10-40 represents a set of three parametric equations for the individual curve coordinates

## Slide 13: BEZIER CURVES AND SURFACES
As a rule,
  a Bezier curve is a polynomial of degree one less than the number of control points used:
    Three points generate a parabola,
    four points a cubic curve, and so forth.

## Slide 14: Some Examples

## Slide 15: Properties of Bezier Curve
1# A very useful property of a Bezier curve is that it always passes through the first and last control points.
  That is, the boundary conditions at the two ends of the curve are
2# Values of the parametric first derivatives of a Bezier curve at the endpoints can he calculated from control-point coordinate as

## Slide 16: Properties of Bezier Curve
3# The parametric second derivatives of a Bezier curve at the endpoints are calculated as
4# Another important property of any Bezier curve is that it lies within the convex hull (convex polygon boundary) of the control points

## Slide 17: Properties of Bezier Curve
5# The sum of Bezier blending function is 1

## Slide 18: Cubic Bezier Curve
Cubic Bezier curves are generated with four control points.
The four blending functions for cubic Bezier curves, obtained by substituting n = 3 into Eq. 10-41.
How???